The Load Sensor
The top piece of plywood rests on the four load sensors
Side view
5mm
2.7 mm
3mm
21mm
5mm
Bottom view
24mm
8mm
The sensor “C” shape (White here) must be supported,
but the (gray here) “T” shape must be free to bend downward, below the “C” shape.

---
The Load Sensor support block,
which sits underneath the load sensor
See loadsensorholder.FCStd
for hole dimensions.
Whatever
You like
Holes to mount the block to the plywood base
Note: the block is made of
two thicknesses of the plywood
used to make the top and
bottom of the scale.
0.70”
(17.8mm)
Note: the block must be thick
Enough that the connectors
will not interfere with the top
piece of plywood.
Whatever
You like
0.55”
(14mm)
1.5”
(38 mm)
Top view
Front view

---
Finding the Center of Gravity

---
Marking the Top Plywood
Center of Gravity
It's important that the top plywood piece of the scale have a center of gravity that is directly over the center of the rectangle formed by the 4 Load Sensors. Any error in the position of the center of gravity will affect your calibration.
NOTE: because plywood isn't of uniform density (like MDF is), the center of gravity is likely not the center of the circle you cut out. So you have to find the center of gravity.

---
Find one line through
the center of gravity
One property of the Center of Gravity is that if you suspend the object (the plywood circle) from a point, the Center of Gravity will be directly below it.
Drill a small hole on the rim of the plywood top. Put a nail loosely through the hole and hang a weight on a string from that nail. Both the plywood circle and the weight must hang freely.
Mark the line you've found this way. The center of gravity will be somewhere along it.

---
Find a second line through
the center of gravity
Drill a second small hole on the rim of the plywood top, about ¼ of the way around the rim from the first hole (but you don't have to be precise). Put a nail through the hole and hang a weight on a string from that nail. Both the plywood circle and the weight must hang freely.
Mark the line you've found this way. The center of gravity will be at the intersection of this line and the first line.
Center of Gravity