The scale design uses one Load Cell Amplifier per Load Sensor (4 total).
These slides describe:
1) how to connect 1 load sensor to an amplifier
2) how to calibrate 4 independent load sensors
3) how to calculate weight and center of gravity

---
The Load Sensor Circuit

---
The Load Sensor circuit
E+ (Vcc)
Black
R1
R1 decreases slightly with weight
S+
Red (S+) voltage should increase with weight
Red
R2
R2 remains constant with weight
E- (GND)
White

---
A Wheatstone Bridge
E+ (Vcc)
R1
R3
S+
S-
R2
R4
The Load Sensor
E- (GND)

---
An easier way to think about
a Wheatstone Bridge:
It is two voltage dividers
5V E+
5V E+
R1
R3
V1 S+
V2 S-
R2
R4
GND E-
GND E-
V1 = V2 only if 5V / (R1 + R2) * R2 = 5V / (R3 + R4) * R4. That is, R1:R2 as R3:R4

---
Using a Load Cell Amplifier
5V
5V
Tiny differences in V1-V2 are amplified.
A slight change in R1 and R2 causes a slight change in V1, which causes a change in (V1-V2) * 128.
That final value is digitized and reported by the HX711. That value is proportional to the change in R1 and R2, which is proportional to the weight on the Load Sensor.
R1
R3
V1
V2
R2
+
-
R4
GND
GND
(V1-V2) * 128

---
Choosing R3 and R4
Because the Load Sensor's R1 is closely matched to R2, we must choose R3 and R4 to be nearly equal to each other. If they aren't, there will be a large voltage difference between V1 and V2, and the amplified difference will be too large to digitize.
A pair of +/-0.1%, 1K resistors may vary by as much 2 ohms (1 + 1 ohm), so we buy several 0.1% 1K resistors and pick a pair of them that are very close to the same resistance.
5V
5V
R1
R3
V1
V2
R2
R4
GND
GND
(V2 – V1) * 128

---
Measuring a resistor pair
E+ Amp RED
Measure the difference in a pair of resistors in the following way:
1) Pick two resistors from the set of 1K ohm, 0.1% resistors. Mark or note which ones they are.
2) Put them in this circuit as RA and RB.
3) Measure the Load Cell Amplifier output with no weight on the Load Sensor. Call that Vab.
4) Swap RA and RB
5) Measure the output again. Call that Vba.
6) The error is |Vba – Vab|
Do this with several resistors and pick the pair that has the minimal difference.
Black
R1
RA
S+
Amp WHT)
Red
S-
Amp GRN
R2
R4
White
E- (Amp BLK)

---
Calibrating 4 separate load sensors.
This scale design calls for a separate amplifier for each load sensor, letting the Arduino see the value for each separate load sensor instead of mixing the 4 load sensors' output with a Load Sensor Combinator Board.

---
Calibrating one Load Sensor
The HX711 library assumes that the resistance of the load sensor
changes linearly with the weight applied to it.
Formula for a line: Y = M * X + B
X is Weight
Y is reported raw value from the amplifier.
Given two {X, Y} pairs, you can calculate M (SCALE) and B (OFFSET):
M = (X2 – X1) / Y2 – Y1)
B = Y1 – M * X1

---
Calibrating 4 Load Sensors:
put the weight at the center
of the rectangle
When a weight W is an equal distance from the 4 Load Sensors A B C and D, each Load Sensor sees ¼ of the weight.
Place a known weight in the center of the scale, and read the values from the Load Sensors A B C and D. Separately record X (W/4), and Y for each Load Sensor.
Repeat the process for at least one more weight.
Then calculate M (SCALE) and B (OFFSET) separately for each Load Sensor.
D
C
W
A
B

---
Measuring Weight and Center of Gravity
from the readings from the 4 Load Sensors

---
Background:
The statics of “Class 1 levers”
The weight on the two support points must sum to the weight placed anywhere between them.
W
W1
W2
W = W1 + W2
Also, as in a seesaw, a fulcrum with two weights, the Moments must sum to zero.
L1
L2
W1
W2
W1 * L1 = W2 * L2

---
Calculating weight W
and center of gravity {X,Y}
Given the weights read by the
Load Sensors A, B, C, and D
and knowing the scale dimensions
U and V, calculate X, Y, and W.
W = A + B + C + D
To calculate X and Y, we use a
property of the center of gravity:
that for any line going through the
center of gravity, the Moments on
one side of the line balance (equal)
those on the other side of the line.
D
C
V
W
Y
A
B
X
U

---
Calculating X
Imagine a knife-edged fulcrum is
under the line PQ. Because PQ goes
through the center of gravity, the
Moments perpendicular to that line
segment must sum to zero.
AX + DX = C(U-X) + B(U-X)
so
AX + BX + CX + DX = CU + BU
so
X = (C + B) / (A + B + C + D) * U
D
C
Q
W
P
A
B
X
U

---
Calculating Y
We calculate Y in the same way
we calculated X:
Imagine a knife-edged fulcrum is
under the line RS. Because RS goes
through the center of gravity, the
Moments perpendicular to that line
segment must sum to zero.
AY + BY = C(V-Y) + D(V-Y)
so
AY + BY + CY + DY = CU + DU
so
Y = (C + D) / (A + B + C + D) * V
D
C
V
W
R
S
Y
A
B

---
The Dog's center of gravity and weight
What we've measured so far is the weight and center of gravity of the combined plywood top plus Pippa (the dog).
To calculate the location of Pippa's center of gravity and her weight, we have to do one more lever calculation: Imagine a fulcrum at W
T * L1 = P * L2
W = T + P
We know T (plywood weight) from calibration.
We know L1 and W from our calculations from A, B, C, and D.
Find P (Pippa's weight) and L2.
So
P = W – T
L2 = T * L1 / P
From there we can use vector addition to calculate the X and Y of Pippa's center of gravity
D
C
T
W
P
L1
L2
A
B