# Arduino 101 continuous weight scale Project Diary
Brad Needham
Begun April 3, 2016

## Summary
I want to automatically weigh our dog every night while she sleeps in her bed. I plan to send the weight via the Arduino 101 (Curie) BLE (Bluetooth Low Energy) radio. Eventually I want to build an Edison or Pi BLE gateway that will use WiFi to send the measured weight to a cloud such as Sparkfun's data server.
I plan to create a scale that is large enough to put our dog's bed on. By continuously reading the weight, the Arduino Sketch can tell when the dog is in the bed, and weigh only when she's been in bed, at rest, for a while.
## Status
The electronics circuit is complete. Now I need to figure how all this will mount to the bottom plate of the scale.
A MakeZine article about continuously weighing a beehive sounds like a similar project: http://makezine.com/projects/bees-sensors-monitor-hive-health/. It uses https://data.sparkfun.com/ to store its data and make it available to everyone for analysis.
## April 3, 2016 – Initial design, cut bottom plywood circle
I'm assuming a few things to make this possible:
- Her bed is a good place to weigh her. I suppose I could put the scale under her crate, but she spends more time in her bed than in her crate.
- She usually doesn't take toys or other animals to bed, so the maximum minus minimum weight will be her true weight. If she brought things into her bed, the weight measure would be complicated.
- Even though she moves around the room in the night, she spends at least a few minutes asleep in her bed every night, so that's a good time to weigh her.
- Although she sometimes sleeps with her head hanging over the edge of the bed, it never touches the floor. If it did, I wouldn't get a good weight reading.
- I'll have to see whether her bed cover touches the floor. I'm assuming it doesn't.
I've ordered and received parts from Sparkfun (see BillOfMaterials.ods). Helpfully, Sparkfun sells a pair of boards that take most of the work out of the electronics. Also, each load sensor has a maximum reading of 50Kg. That's over 110 lbs, which is over 2 times the weight of our dog. Since there are 4 sensors, which will split the load depending on where the center of gravity is, it seems nicely over-designed to support her weight.
I plan to buy two sheets of plywood: one for the base, that will contain the load sensors and electronics, and one that will sit on top of the load sensors.
The challenge at this point is to design the mechanical parts.
- Each load sensor needs to be supported only on its outside arms; the center arm must be free to bend – that arm is where the strain sensor is attached.
- Each load sensor has a small metal bump on top. The upper piece of wood must rest on all four of these bumps, and must not slip off. I'm not quite sure how to arrange that yet. I suppose I might drill 4 small dents into the upper piece of wood so that it won't slip over the bump.
- To prevent the top piece from slipping off when bumped, I'm thinking of attaching sides to it, so that the top piece is sort of a wooden box lid with sides that go down to part of the lower part.
- The wires that come attached to the load sensors are likely too short, so I'll need to solder-and-heat-shrink some longer wires to them. I'm a little concerned that long wires may pick up electrical noise that may make it difficult to make an accurate reading. Perhaps I can move the load sensors somewhere between the corners of the bottom board and the center, and not have to add extra wire.
Measured our dog's bed: a roughly-circular 41-inch diameter (~20” radius) shape. The wires on each load sensor are about 15 inches from the edge of the sensor to the end of the wire. That makes a roughly 30” square with sensors on the sides, which sounds pretty good.
I worried for a moment that all of the dog, bed, and covers must be inside the rectangle defined by the load sensors, but now I don't think that's true: it doesn't matter to the weight measurement where the weight is, as long as the center of gravity is within the rectangle.
Privacy: Imagining putting per-minute-or-so weight data on a server available to anyone makes me think a moment about what such data could unintentionally reveal: when we go to bed and get up; when she's in boarding (that is, when we're away). Naively it doesn't sound like it could reveal much else.
I measured the dog bed and decided to make a 41” circular scale, with the load sensors near the edge. I realized that when Pippa sleeps against one side of her bed, her center of gravity could be close to the edge. Because of that situation, I need to put the load sensors as close to the outside edge of the circle as I can.
Bought 2 sheets of 4'x4'x3/4” plywood. 1/2” seemed to flex too much; 3/4” didn't flex with the weight I'm planning on.
Using a beam compass I'd purchased a long time ago, I drew a 41” diameter circle on the first plywood sheet, then cut it with a jig saw.
## April 5, 2016 – solder wire extensions
The load sensors come with about 15” of wire attached. I need closer to 26” of wire, so I soldered on another 14” of wire to each wire. I happened to use some CAT3 cable I had lying around, but you could use separate, stranded cable to extend the load sensors' wires.
## April 6, 2016 – Solder headers; puzzle out the circuit
I soldered headers on all the pins of the Load Combinator board and the Load Cell Amplifier board. I did this instead of soldering the wires directly to make it easy to correct wiring errors and to replace a failed part.
Next I wanted to crimp the female connectors onto the load sensors, but was a bit stumped about which pin to connect where. The Load Combinator board pins are labeled B, W, and R, and the load sensor wires are Black, White, and Red, so I could just wire B to Black, etc., but I've seen enough cheap parts that have swapped wires that I'd like to understand the schematic.
So first I measured the resistance of a load sensor. B to R was about 1Kohm, R to W was about 1Kohm, and B to W was about 2Kohm. So the Red wire in the sensor is the center tap between two resistors. Further, as I pushed on the sensor, the resistance between R and B dropped a little, and the resistance between R and W stayed the same. Reading through Sparkfun's Load Cell Amplifier Hookup Guide, I found a description of the load sensor, that matched what I'd seen. So this gives me confidence that I can connect each Load Sensor to the corresponding B, W, and R pins on the Load Combinator board.
## April 7, 2016 – Complete the wiring
I finished crimping all the connectors to various wires. Now the circuit is complete. In summary: I've soldered and heat-shrunk extensions to each of the load sensors' wires; I've soldered in header pins for all the connections on the Load Combinator board and Load Cell Amplifier board; I've crimped 3-pin connectors on the end of each set of 3 wires for each load sensor; I've crimped 4-pin connectors between the Load Combinator and Load Cell Amplifier boards; I've crimped a 4-pin connector onto the wires that go from the Load Cell Amplifier board to the Arduino.
For now I'm using an Arduino Uno, because I want to check that the code works on an Uno before seeing whether I need to do anything to port to Arduino 101. I also decided to put the Arduino on the bottom plywood piece of the scale, along with the other electronics. I'll need to remember to open and vacuum the scale every once in a while, to keep dust from short-circuiting the parts.
I also test layed out the parts on the bottom circle of plywood. Everything looks good. I'm still a bit puzzled about how to keep the load sensors from slipping without epoxying them down.
## April 9, 2016 – design a preliminary support block
I measured the dimensions of the load sensor, documented them in the Mechanical Notes file, and worked out the preliminary design of the block that will support the load sensor and keep the top piece of plywood from pressing on the circuitry (which is rather thick because of the connectors). This preliminary block will allow me to test the rest of the circuit while I think about a more permanent design that will keep the load sensors from slipping over time.
## April 10, 2016 – Assemble and test the scale, discover a problem
Today was a second day of woodworking: I cut the top circular piece of plywood; drilled mounting holes for the Combinator board, the Load Cell Amplifier board, and the Arduino; counterbored holes in the bottom of the plywood base so the board nuts can connect; cut out blocks to support the load sensors (with nothing to hold them in place yet); assembled the whole thing and turned it on.
The great news is that it seems to work, and seems to be wired correctly!
I did a few tests using the Sparkfun HX711 examples, and found a few things:
- The HX711 library assumes a linear change in readings vs. weight (vs. say polynomial). Something is funny, because the code seems to scale the value differently depending on what 'zero' weight is on the scale. That suggests the sensors' values aren't linearly proportional to weight. I'll have to explore this more.
- The position of Pippa's center of gravity on the scale will produce different readings. This is a big problem, since Pippa often sleeps with her head hanging over the edge of her bed.
Moving a 15 pound weight from the center to the 4 corners (right above each of the 4 load sensors) gave readings that differed by a few pounds. This tells me the load sensors don't all have the same calibration factor, or perhaps aren't wired identically. This isn't surprising, since each load sensor is labeled with a different calibration factor. This means that as Pippa moves around in bed, the scale will produce different (incorrect) values. I have to explore this more once I get the basic scale calibrated and working properly.
I'm so happy I connected everything with connectors rather than soldering it together, because it looks like I'll need to change the circuit design to accommodate Pippa sleeping in different parts of the bed – that is, with her center of gravity anywhere inside the rectangle defined by the points of the four load sensors.

Next steps:
- Find the load-at-center calibration factor by using various code from the HX711 library and the Sparkfun examples.
- Consider redesigning the scale to use 4 load Cell amplifiers so that I can compensate for the different calibration factors of the different load sensors. Doing that would also give some information about where Pippa is lying in her bed (at one side vs. near the center), which would be useful to know.